## Slide 1
OSCILLATION → FREQUENCY → AC SIGNAL
Course Code: CSE 1205
Course Title: Electrical Engineering and Circuit Analysis
Presented to Lecturer Dr.Mst. Najnin Sultan
Assistant professor, NUB dept. CSE
ARUNAV BISWAS
SID:41250303008
SADIYA ISLAM
SID: 41250303090
Presentation content is based on the reference material available in the provided Google Drive document CLICK HERE

## Slide 2
This Presentation Covers
1. Oscillation
The natural, source-free behavior of L-C energy exchange in second-order circuits.
2. Frequency Generation
Resonance, LC tanks, feedback oscillators, and the Barkhausen criterion.
3. AC Signal Generation
Sinusoids, phasors, and the practical generation of usable AC signals.
4. Applications & Synthesis
How the three ideas connect, and where they are used in real systems.

## Slide 3
INTRODUCTION
This Topic Matters
Oscillatory circuits generate stable periodic signals.
Energy exchange between L and C produces oscillation.
Circuit parameters determine the oscillation frequency.
Feedback sustains oscillations and generates AC signals.
Based on Alexander & Sadiku and Boylestad circuit analysis concepts.

## Slide 4
OSCILLATION 1.1
The Physical Basis of Oscillation
Inductor stores energy in a magnetic field; capacitor stores energy in an electric field.
Energy continuously transfers between L and C, creating oscillation.
Similar to energy exchange in a mass-spring or pendulum system.
Resistance causes energy loss as heat.
Therefore, passive RLC oscillations gradually decay over time.
wʟ = ½ L i² (energy stored in the inductor's magnetic field)
wᴄ = ½ C v² (energy stored in the capacitor's electric field)

## Slide 5
Source-Free Series RLC Circuit
Applying KVL to a series R-L-C loop gives a 2nd-order differential equation.
Its characteristic-equation roots are:
s₁,₂ = −α ± √(α² − ω₀²) α = R / 2L ω₀ = 1 / √(LC)
Overdamped
α > ω₀
Two real, distinct roots. The response decays to zero with no oscillation at all.
Critically Damped
α = ω₀
Two equal real roots. The fastest possible decay without any oscillation.
Underdamped
α < ω₀
Complex roots, s = −α ± jωd. A genuine — though decaying — oscillation appears.
OSCILLATION 1.2

## Slide 6
Underdamped Response: A Damped Oscillation
OSCILLATION 1.3
Chart: Decaying sinusoid: v(t) = e⁻ᵃᵗ cos(ωd t)
| 0.0 | 0.5 | 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0 | 5.5 | 6.0 | 6.5 | 7.0 | 7.5
v(t) | 1 | 0.38077 | -0.41471 | -0.58415 | -0.15262 | 0.29542 | 0.33252 | 0.045055 | -0.20001 | -0.18407 | 0.00076907 | 0.1303 | 0.098686 | -0.016665 | -0.082234 | -0.050881
Damped frequency: As resistance decreases, damping decreases.
When , and oscillations persist.
This lossless condition forms the basis of frequency generators.
Figure 1(a) illustrates the decaying oscillatory (ringing) response of an RLC circuit.
Figure 1(a): Damped oscillatory response (ringing) of a second-order RLC circuit.

## Slide 7
FREQUENCY GENERATION 2.1
Resonance: The Frequency-Fixing Mechanism
ω₀ = 1 / √(LC) Q = ω₀ / B B = ω₀ / Q
Resonance occurs when , making the circuit purely resistive.
Resonant frequency: .
At resonance, the circuit response reaches its maximum value.
Quality Factor () indicates the sharpness of the resonance peak.
Higher → narrower bandwidth and better frequency selectivity.
Bandwidth: .
Resonance enables the generation of a clean, stable frequency.

## Slide 8
FREQUENCY GENERATION 2.2
Series vs. Parallel Resonance
Source: Alexander & Sadiku, Ch. 14 “Frequency Response” (Series/Parallel Resonance); Boylestad, Ch. 20 “Resonance,” p. 879.
Characteristic | Series Resonant Circuit | Parallel Resonant Circuit
Resonance condition | Xʟ = Xᴄ (reactances cancel) | Bʟ = Bᴄ (susceptances cancel)
Impedance at ω₀ | Minimum (Z = R) | Maximum (Z = R)
Peak quantity | Current is maximum | Voltage is maximum
Typical role | Acceptor / band-pass selection | Rejector circuits, oscillator tank circuits

## Slide 9
FREQUENCY GENERATION 2.3
The LC Tank Circuit
A tank circuit consists of a parallel inductor (L) and capacitor (C).
Energy continuously exchanges between L and C, producing oscillation.
Ideal tank circuits oscillate indefinitely at .
Real tank circuits experience losses due to resistance and dielectric effects.
Oscillations gradually decay unless lost energy is replenished.
Sustaining oscillation requires compensating for energy lost each cycle.

## Slide 10
Sustaining Oscillation: The Barkhausen Criterion
FREQUENCY GENERATION 2.4
Active devices supply energy to compensate for circuit losses.
Feedback must be in phase with the oscillation.
Barkhausen Criterion: Loop gain = 1 and phase shift = 0° (or 360°).
Proper feedback maintains a constant oscillation amplitude.
Resonant network sets the oscillation frequency .
Feedback network sustains oscillation by offsetting losses.

## Slide 11
Types of Practical Oscillators
1
RC Phase-Shift Oscillator
A chain of R-C sections gives the 180° phase shift needed (with an inverting amplifier) to satisfy Barkhausen. Common for audio-range frequencies.
FREQUENCY GENERATION 2.5
2
3
4
Wien-Bridge Oscillator
An RC bridge network feeding a non-inverting amplifier; widely used in low-distortion, audio-frequency function generators.
LC tank-based designs for radio frequencies; Colpitts taps the capacitor, Hartley taps the inductor, to form the feedback path.
Colpitts / Hartley Oscillators
Crystal Oscillators
Replace the LC tank with a piezoelectric quartz crystal of extremely high Q — the timing reference for clocks, microprocessors, and communication gear.

## Slide 12
Frequency Response, Transfer Functions & Bode Plots
Chart: Resonant magnitude response |H(ω)| vs. ω/ω₀ (Q = 5)
| 0.1 | 0.25 | 0.5 | 0.75 | 1 | 1.5 | 2 | 3 | 5 | 8
¦H(ω)¦ | 0.020198 | 0.053258 | 0.13216 | 0.32432 | 1 | 0.23337 | 0.13216 | 0.07479 | 0.041631 | 0.025389
FREQUENCY GENERATION 2.6
Transfer Function : Output-to-input ratio in the frequency domain.
Bode Plots: Show gain and phase variation with frequency.
Design Verification: Confirm Barkhausen conditions at .

## Slide 13
AC SIGNAL GENERATION 3.1
Characterizing the Sinusoidal Signal
Once a frequency is fixed, the resulting signal is described by three parameters:
Vₘ — Amplitude
The peak value of the sinusoid; sets the signal's strength.
ω — Angular Frequency
ω = 2πf, in radians per second; sets how fast the signal repeats.
Shifts the waveform in time relative to a reference; sets timing alignment.
φ — Phase Angle
v(t) = Vₘ cos(ωt + φ)

## Slide 14
Practical AC Signal Sources
AC SIGNAL GENERATION 3.2
Function / Signal Generators
Packaged oscillator circuits with adjustable frequency, amplitude, and waveform (sine, square, triangular).
Voltage-Controlled Oscillators (VCOs)
Output frequency varies with a control voltage — the basis of FM and phase-locked-loop frequency synthesis.
Phase Shifters
Introduce a controlled lag or lead between two AC signals (Alexander & Sadiku, Sec. 9.8.1, p. 394).
AC Bridges
Compare an unknown impedance against a known AC reference signal (Alexander & Sadiku, Sec. 9.8.2, p. 394).

## Slide 15
APPLICATIONS
Real-World Engineering Applications
Communication Systems: Carrier generation, modulation, and tuning.
Digital Systems: Clock generation for processors and microcontrollers.
Power Electronics: Frequency control in inverters and SMPS.
Instrumentation: Function and signal generators for testing.
Industrial & Biomedical: Induction heating and ultrasonic systems.

## Slide 16
SYNTHESIS
How the Three Topics Connect
Oscillation
Resonance
Feedback
AC Signal
Natural L–C energy exchange (Sec. 1)
Fixes the exact rate ω₀ (Sec. 2)
Barkhausen sustains it forever (Sec. 2)
Usable, phasor-describable output (Sec. 3)
Oscillation is the physics, resonance and feedback are the engineering, and the AC signal is the payoff — analyzable end-to-end with phasors and frequency-response tools.

## Slide 17
CONCLUSION
One Continuous Idea, Not Three Separate Topics
Energy-storage elements (L, C) naturally exchange energy at a characteristic rate — this is oscillation.
Resonance and active feedback fix that rate precisely and sustain it indefinitely — this is frequency generation.
The resulting periodic signal, represented through phasors and shaped with frequency-response tools, becomes the working AC signal that powers communication, computing, and instrumentation.
Alexander & Sadiku’s second-order circuit analysis, resonance theory, and phasor methods — together with Boylestad’s treatment of sinusoidal waveforms and resonance — supply the complete toolkit for every stage of this chain.

## Slide 18
REFERENCES
Primary Course Texts & Page References
Alexander, C. K., & Sadiku, M. N. O. — Fundamentals of Electric Circuits (6th/7th ed.), McGraw-Hill
Ch. 8, “Second-Order Circuits” — pp. 311–365 (Source-Free Series RLC, p. 317; Source-Free Parallel RLC, p. 324; Step Responses, pp. 329 & 334; Duality, p. 348).
Ch. 9, “Sinusoids and Phasors” — pp. 367–409 (Sinusoids, p. 369; Phasors, p. 374; Impedance/Admittance, pp. 383–387; Applications, p. 394).
Ch. 10, “Sinusoidal Steady-State Analysis” — from p. 411/412 (Applications Sec. 10.9, incl. 10.9.2 “Oscillators”).
Ch. 14, “Frequency Response” — Transfer Function, Decibel Scale, Bode Plots, Series/Parallel Resonance, Filters.
Boylestad, R. L. — Introductory Circuit Analysis (12th ed.), Pearson / Prentice Hall
Ch. 13, “Sinusoidal Alternating Waveforms” — p. 545.
Ch. 14, “The Basic Elements and Phasors” — p. 595.
Ch. 15, “Series and Parallel ac Circuits” — p. 645.
Ch. 20, “Resonance” — p. 879.